## Slide 1
SLIPS, TRIPS, AND FALLS
Safety Sheets

## Slide 2
These Safety Sheets are training materials to help prevent Slips, Trips and Falls on CEMEX premises and during work activities.
The Safety Sheets are divided into two sections.
The first part is dedicated to raising risk awareness of STF – most frequent causes of injuries, basic counter measures and safe behaviour.
The second part is a self assessment checklist that you can use for evaluation of STF at your sites.
NOTE:
These guidelines do NOT replace local laws, CEMEX standards, or other internal guidelines that must also be followed.

## Slide 3: Identifying Risk
Every CEMEX employee, contractor, visitor, and customer on CEMEX premises is at risk of slipping, tripping or falling.
Lack of housekeeping
Unsafe behaviour
Poor conditions of workplaces, roads and walkways
Unsafe behaviour
Not secured workplace
Poor lighting

## Slide 4: Safe Behaviour
Stop and Think. Warn others of dangerous behaviour.
Get a Grip. Hold the hanrail while walking.
Wear properly laced safety boots.
Report Near Misses / Hazards in INTELEX
When was the last time you…?
Reminded others to act in a safe way?
Didn´t hold the handrail?
Worked with your boots not properly laced up?
Reported a Near Miss / Hazard?
TAKE CARE OF YOUR SAFETY AND ENCOURAGE OTHERS.

## Slide 5: Railings, Openings in Floors
All elevated permanent work sites
(1.5 m above the surrounding level) shall be fitted with a 110 cm handrail and equipped with a toe board.
Take 5 for a quick check. Your safety matters. |  | 
WHAT CAN YOU CHECK? | IS EVERTHING OK? | IS SOMETHING WRONG?
Are railings in good shape and high enough? Is nothing missing? |  Yes /  No /  Partially | 
Are all openings in floors protected? Are hatches closed and robust? |  Yes /  No /  Partially | 
All openings in floors must be secured against falls.
Holes in floors that cannot be covered must be surrounded by handrails and marked.
Fixed ladders must have
a fall-prevention gate at the exit point.

## Slide 6: Ladders, Scaffolding
Ladders must always be in good working condition. Visually inspect them before each use. They should be formally inspected with records in place.
Scaffolding must be in a good working condition and equipped with all elements (kickplates, railings, access ladders, etc.). The working condition of the scaffolding must be checked regularly. The scaffolding must be inspected weekly and marked as safe for use.
Ladder inclination must be between 65-75 °.
The ladder must overlap at least 1.1 m at the exit/entry point.
The ladder must be secured against slipping.
Ask yourself one question. It can spare you weeks in hospital
WHEN WAS THE LAST TIME YOU CHECKED YOUR LADDER?

## Slide 7: Ladders, Scaffolding, Railings
Only authorized persons can enter the scaffolding.
Always use three contact points when climbing up or down a ladder.
Do not raise the work site by using unstable objects or by using the scaffolding construction.
Do not carry out work that requires you to lean over the sides of the ladder.
Any damage to the scaffolding must be reported. Do not remove any scaffolding parts.
Do not carry loads on ladders.
Do not use dangerous tools on ladders.
Space for self-reflection
WHAT CAN I CHANGE TO STAY SAFE?

## Slide 8: Housekeeping, Personal Protective Equipment
Use non-slip gloves in case of risk.
Work sites and roads must be kept clean for pedestrians.
Store equipment and tools at designated locations.
Pedestrian routes must be free of potholes, ice and snow.
Risk areas in the work site must be clearly marked.
Always use suitable boots that are in good condition at work sites. Always wear properly laced boots.
Ready for working safely? | 
DO YOU HAVE…? | 
All tools stored at designated place |  Yes /  No
Proper boots |  Yes /  No
Tools for keeping workplaces and roads clean |  Yes /  No

## Slide 9: Vehicles, Work on the Top of Vehicles
There are fixed or mobile platforms for safe access to trucks.
If they cannot be accessed from the platform, safe access to the vehicle must be ensured.
When entering and exiting the vehicle use three points of contact and face the vehicle.
(Be careful when descending onto an uneven surface.)
Enter the loading area only by ramp, ladder, etc. Never jump.
Are you a driver? Take a quick check. |  | 
WHAT CAN YOU CHECK? | IS EVERTHING OK? | IS SOMETHING NOT OK?
Is the platform on your truck in good condition? |  Yes /  No /  Partially | 
Are sites where you usually deliver material equipped safe for unloading? |  Yes /  No /  Partially | 

## Slide 10: Slips, Trips and Falls Self Assessment
Safe Behaviour |  |  |  |  |  | 
REQUIREMENTS | IS EVERTHING OK? |  | WHAT IS WRONG | HOW WE WANT TO FIX IT | WHO WILL BE RESPONSIBLE | WHEN WE WANT TO FINISH
Do employees use unsuitable alternatives for ladders or steps (e.g. Cases, boxes, chairs)? |   | Yes Partially |  |  |  | 
 |  | No |  |  |  | 
Do all employees and contractors use three points of contact while getting out / in of a truck or while using a ladder? |   | Yes Partially |  |  |  | 
 |  | No |  |  |  | 
Do all employees and contracotors wear appropriate safety boots and gloves, adapted to the activity (e.g. anti-slip)? |   | Yes Partially |  |  |  | 
 |  | No |  |  |  | 

## Slide 11: Slips, Trips and Falls Self Assessment
Safe Workplace |  |  |  |  |  | 
REQUIREMENTS | IS EVERTHING OK? |  | WHAT IS WRONG | HOW WE WANT TO FIX IT | WHO WILL BE RESPONSIBLE | WHEN WE WANT TO FINISH
Are traffic routes and permanent workplaces where people may walk free from hazardous protruding elements of structures, machinery or equipment that could cause a trip and a fall? |    | Yes Partially No |  |  |  | 
Are other protruding elements of structures, machinery or equipment that are located on traffic routes and cannot be removed properly marked with safety colours (e.g. black and yellow)? |    | Yes Partially No |  |  |  | 
Are traffic routes and permanent workplaces where people may walk, free from structural hazards (eg holes, edges, gaps, other irregularities)? |    | Yes Partially No |  |  |  | 
Are the hazardous steps or other hazards like edges, slopes, etc. that are located on traffic routes marked with safety colours (e.g. black and yellow)? Has it been checked, if hazardous steps can be avoid or replaced? |    | Yes Partially No |  |  |  | 

## Slide 12: Slips, Trips and Falls Self Assessment
Housekeeping |  |  |  |  |  | 
REQUIREMENTS | IS EVERTHING OK? |  | WHAT IS WRONG | HOW WE WANT TO FIX IT | WHO WILL BE RESPONSIBLE | WHEN WE WANT TO FINISH
Are non-slip surfaces, without rain water, sewage waste or process spillage, provided on traffic routes and in permanent workplaces? |    | Yes Partially No |  |  |  | 
Are stairs and platforms with railings in good technical condition, without damage? |   | Yes Partially |  |  |  | 
 |  | No |  |  |  | 
Is site housekeeping good? Are pedestrian walkways free from "movable“ trip and fall hazards (e.g. cables, hoses)? |    | Yes Partially No |  |  |  | 

## Slide 13: Slips, Trips and Falls Self Assessment
Ladders, Scafolding, Platforms |  |  |  |  |  | 
REQUIREMENTS | IS EVERTHING OK? |  | WHAT IS WRONG | HOW WE WANT TO FIX IT | WHO WILL BE RESPONSIBLE | WHEN WE WANT TO FINISH
Are portable and fixed ladders in compliance with the standards and regulations as well as in good technical condition, without damage? |    | Yes Partially No |  |  |  | 
Are mobile platforms / mobile scaffolding properly contructed according to instructions? Is there a manual available? Are the employees instructed in using mobile scaffolds? Is the mobile plattform / scaffolding heigh enough for the work and without damage and in a good condition? |    | Yes Partially No |  |  |  | 
Is there a effective side protection (e.g. for scaffolds, plattforms) with three pieces (handrail, mid rail, toe plate)? Are railings and handrails heigh enough? |    | Yes Partially No |  |  |  | 
 |  | Yes |  |  |  | 
Is the lighting at stairs sufficient? |  | Partially |  |  |  | 
 |  | No |  |  |  |